## Slide 1
Parallel Simulation of Microplastic Dispersion Using Ocean Current Data
IT 301 - Parallel Computing
National Institute of Technology
Karnataka Surathkal

## Slide 2
INTRODUCTION
Microplastic in every ocean basin
Studied by Lagrangian particle tracking
Particles are passive tracers in a current field
Each particle advanced at every timestep
Velocity rebuilt by interpolation each step
PROBLEM STATEMENT
Millions of particles, months of simulated time
Too slow to run serially
Need parallelism on ordinary hardware

## Slide 3
BACKGROUND
How the Simulation Works
At each timestep the simulation keeps the two current-field time slices that bracket the model time. For every particle it interpolates the velocity bilinearly over the surrounding grid cells and linearly between those two slices, then advances the position with a fixed-step Runge–Kutta step. The positions are accumulated into a density grid, which becomes the dispersion map at the end of the run.
Existing Work
Lagrangian frameworks on reanalysis data
Advection matches observed transport
Used to locate the subtropical gyres
Aim is accuracy, not speed
Research Gap
Advection run serially or on clusters
Thread behaviour rarely reported
Speedup and efficiency not published
No matched serial-vs-parallel baseline

## Slide 4
METHODOLOGY
Building the Simulation
Read ocean current data into a time-indexed velocity grid
Seed particles at chosen release points
Per timestep: interpolate velocity, take the Runge–Kutta step
Record positions into a density grid
Parallelising and Measuring
Write and verify the serial baseline first
Parallelise the particle loop with OpenMP
Keep density bins per-thread, merge at step end
Time both versions on identical inputs
Sweep particle count, resolution and thread count

## Slide 5
MOTIVATION / USE CASES
Why Runtime Is the Limit
Cost = particles × timesteps
A serial run forces a cut:
  fewer particles → noisy patterns
  coarser grid → eddies lost
Sensitivity studies get dropped
Who Benefits
Researchers — faster experiments
Coastal agencies — beaching zones
Policymakers — cleanup priorities

## Slide 6
NOVELTY
The transport model is standard; the parallel implementation is where our work is.
The novelty is in combining the two — a current-driven dispersion simulation built as a parallel program.
The advection loop is parallelised over the particles with OpenMP, since they are independent within a timestep.
Serial and parallel versions run on the same data and numerics, so the speedup is measured, not assumed.
Small code with no simulation framework, so the measured time belongs to the advection kernel.

## Slide 7
EVALUATION PLAN & EXPECTED CONTRIBUTIONS
Computational
Runtime, speedup, parallel efficiency
Vary particles, resolution, threads
Locate the scaling limit
Physical
Patterns match current-driven transport
Parallel output agrees with serial
Expected Contributions
Transport model on real ocean current data
Serial baseline plus parallel kernel
Scalability study across particles and cores
Dispersion maps of accumulation zones

## Slide 8
THANK YOU
Team members:-
Batti Akbarali Abbasali - 241IT014
Dhruv Agrawal - 241IT026
Patil Rigved Ramesh - 241IT052
Salim Moh - 241IT068